## Slide 1
IoT Project • UT
Smart Water Tank
Monitoring & Overflow Prevention System
IoT-based Automated Water Management using ESP8266, Ultrasonic Sensors, MQTT & Servo Automation
ESP8266
MQTT
HC-SR04
Servo
Real-Time
PRESENTED BY
Muhammad Haris Irfan – Muhammad Zain

## Slide 2
01 • CONTEXT
The Real-World Problem
Pakistan • Daily Water Routine
Tanker fills the underground tank. A person manually switches the motor ON, waits for water to reach the rooftop tank, and turns it OFF only after they see water overflowing from the pipe.
Water Wastage
Overflow is the signal — water is already lost.
Human Dependency
Someone must remember to start and stop the motor.
Forgotten Motors
Motor left running overnight is a common mistake.
Routine Overflow
Even ideal operation ends in overflow by design.
“Even in the best-case scenario, overflow water is already wasted water.”
Smart Water Tank Monitoring System
2 / 10

## Slide 3
02 • SOLUTION
Automated Smart Water Tank System
Auto Motor ON
Triggers when water level falls low.
Auto Motor OFF
Stops once target level is reached.
Overflow Safety
Independent sensor catches faults.
Live MQTT Feed
Status published in real-time.
Remote Monitoring
View tank from phone or laptop.
SYSTEM ARCHITECTURE
Underground Tank
Motor (Servo Sim.)
Main Rooftop Tank
Sensors (Level + Overflow)
ESP8266 Controller
MQTT Broker
Mobile / Laptop UI
Smart Water Tank Monitoring System
3 / 10

## Slide 4
03 • BUILD
Hardware Components
ESP8266 Wemos D1 Mini
Wi-Fi controller — runs the logic and talks to MQTT.
HC-SR04 Ultrasonic Sensor
Measures live water level inside the tank.
Water Sensor
Detects overflow as an independent safety trigger.
Servo Motor
Simulates the motor switch — ON / OFF actuator.
Piezo Buzzer
Audible alert when tank is FULL or overflowing.
Breadboard + Wiring
Prototyping platform for all sensor connections.
Smart Water Tank Monitoring System
4 / 10

## Slide 5
04 • WIRING
Circuit Diagram
Signal Line
5V Power
3.3V Power
Ground
Smart Water Tank Monitoring System
5 / 10

## Slide 6
05 • ALGORITHM
System Logic Flow
01
Read Water Level
HC-SR04 measures distance to water surface.
02
Low? Motor ON
If level below threshold, activate motor.
03
Continuous Monitor
Keep reading level while motor runs.
04
Target Reached → OFF
Stop motor when desired level is hit.
05
Overflow Detected?
Independent water sensor fires buzzer alert.
06
Publish to MQTT View on Dashboard
Stream live status to broker each cycle.
Smart Water Tank Monitoring System
6 / 10

## Slide 7
06 • CONNECTIVITY
Live MQTT Monitoring
Real-Time IoT Telemetry
The ESP8266 publishes tank state to an MQTT broker. Any subscriber — phone, laptop, or dashboard — receives instant updates.
ESP8266
publisher
MQTT
broker
Dashboard
subscriber
publish
subscribe
Updates streamed every cycle — under one second latency.
mqtt://broker/tank/status
{
"water_level": 82,
"motor": "OFF",
"status": "FULL",
"overflow": false
}
Sample payload published to the MQTT topic
Smart Water Tank Monitoring System
7 / 10

## Slide 8
07 • DEMO
Live Demonstration
What you'll see in the live demo
Real-Time Water Level Detection
Ultrasonic sensor reports tank height as water fills.
Automatic Motor Control
Servo angle changes as motor switches ON / OFF.
Live dashboard
MQTT messages seen on dashboard refreshes with each new reading.
Serial Monitor Output
Diagnostic stream shows every decision the MCU makes.
Smart Water Tank Monitoring System
8 / 10

## Slide 9
08 • ROADMAP
Future Improvements
Real Relay Control
Drive an actual AC motor in place of the servo.
Dedicated Mobile App
Native iOS / Android control and history.
Cloud Database
Persist tank readings for long-term analytics.
Push Notifications
Alerts when tank is full, leaking, or empty.
Water Usage Analytics
Trends, peak hours, leak detection patterns.
Solar-Powered Node
Off-grid deployment for rural installations.
Smart Water Tank Monitoring System
9 / 10

## Slide 10
CONCLUSION
Small IoT systems,
real-world impact.
“This project demonstrates how simple, low-cost IoT systems can solve real water management problems faced daily in developing countries.”
Smart Home Ready
Drop-in solution for any rooftop tank
Water Conservation
Zero overflow, zero waste
IoT Sustainability
Connected, scalable, low-power
Thank You
Muhammad Haris Irfan
Muhammad Zain